## Slide 1: CSE 301 Microprocessors
Dr. Md. Sujan Ali
Associate Professor
Dept. of Computer Science and Engineering
Jatiya Kabi Kazi Nazrul Islam University
Trishal, Mymensingh, Bangladesh

## Slide 2
Microprocessor Software Concepts

## Slide 3: Instruction
What are instructions microprocessor?
An Instruction is a command given to the computer to perform a specified operation on given data.
The instruction set of a microprocessor is the collection of the instructions that the microprocessor is designed to execute.
The programmer can write a program in assembly language using these instructions.
The first part of each instruction, called MNEMONIC refers to the operation an instruction performs (copy, addition, logic operation etc.). Mnemonics are abbreviations of the name of operation being executed.

## Slide 4: Instruction Formats (cont’d)
What are Instruction formats?
When the assembler processes an Instruction it converts the instruction from its mnemonics* form to standard machine language format called the "Instruction format".
Instruction format describes the internal structures (layout design) of the bits of an instruction, in terms of its constituent parts.
The bits of the instruction are divided into groups called fields.
*

## Slide 5: Instruction Formats (cont’d)
The most common fields found in instruction formats are:
An operation code field that specifies the operation to be performed like addition.
Address field which contain the location of operand, i.e., register or memory location.
A mode field that specifies the way the operand or the effective address is determined.
Operation code | Address field/Operand | Mode field

## Slide 6: Instruction Formats (cont’d)
Zero Address Instruction Format
Zero-address instruction: An instruction that contains no address fields; operand sources and destination are both implicit.
Stack processing (stack manipulation): Use of a pushdown stack or LIFO implemented in hardware as a data memory. This permits the use of zero-address instructions where both operand sources and result destinations are implicitly the top locations of the stack.
Example:
PUSH A TOS←A
PUSH B TOS←B
ADD TOS ←(A + B)
POP X [X] ←TOS

## Slide 7: Instruction Formats (cont’d)
One Address Instructions
This use a implied ACCUMULATOR (AC) register for data manipulation.
One operand is in accumulator and other is in register or memory location.
Implied means that the CPU already know that one operand is in accumulator so there is no need to specify it.
Examples:
LOAD A AC ←M [A]
ADD B AC ←AC + M [B]
Opcode | Operand/Address of operand | Mode

## Slide 8: Instruction Formats (cont’d)
Two Address Instructions
This is common in commercial computers.
Here two address can be specified in the instruction. Unlike one address instruction the result was stored in accumulator here result can be stored at different location rather than just accumulator.
Examples:
ADD R2, D R2← R2 + M [D]
MUL R1, R2 R1← R1∗R2
Opcode | Destination address | Source Address | Mode

## Slide 9: Instruction Formats
Three Address Instructions
This has three address field to specify a register or a memory location.
Program created are much short in size but number of bits per instruction increase.
These instructions make creation of program much easier but it does not mean that program will run much faster because now instruction only contain more information but each micro operation (changing content of register, loading address in address bus etc.) will be performed in one cycle only.
Examples:
ADD R2, C, D R2 ←M [C] + M [D]
MUL X, R1, R2 M [X] ←R1 ∗R2
Opcode | Destination address | Source address 1 | Source address 2 | Mode

## Slide 10: Addressing Modes (cont’d)
Adressing Modes
The operation field of an instruction specifies the operation to be performed.
This operation will be executed on some data which is stored in computer registers or the main memory.
The way any operand is selected during the program execution is dependent on the addressing mode of the instruction.
The purpose of using addressing modes is as follows:
To give the programming versatility to the user.
To reduce the number of bits in addressing field of instruction.

## Slide 11: Addressing Modes (cont’d)
Immediate Mode
In this mode, the operand is specified in the instruction itself.
An immediate mode instruction has an operand field rather than the address field.
Example:
ADD 7
Add 7 to contents of accumulator. 7 is the operand here.
MOV AL, 35H
Move the data 35H into AL register

## Slide 12: Addressing Modes (cont’d)
Register Mode
In this mode the operand is stored in the register and this register is present in CPU. The instruction has the address of the Register where the operand is stored.
Example
MOV AX,CX
Move the contents of CX register to AX register
Advantages
Shorter instructions and faster instruction fetch.
Faster memory access to the operand(s)
Disadvantages
Very limited address space
Using multiple registers helps performance but it complicates the instructions.

## Slide 13: Addressing Modes (cont’d)
Register Indirect Mode
In this mode, the instruction specifies the register whose contents give us the address of operand which is in memory.
Thus, the register contains the address of operand rather than the operand itself.
Example
MOV AX, [BX]
Move the contents of memory location s addressed by the register BX to the register AX

## Slide 14: Addressing Modes (cont’d)
Auto Indexed (increment mode)
Effective address of the operand is the contents of a register specified in the instruction.
After accessing the operand, the contents of this register are automatically incremented to point to the next consecutive memory location.(R1)+.
Example
Add R1, (R2)+

## Slide 15: Addressing Modes (cont’d)
Auto indexed ( decrement mode)
Effective address of the operand is the contents of a register specified in the instruction.
Before accessing the operand, the contents of this register are automatically decremented to point to the previous consecutive memory location.
Example:
Add R1,-(R2)

## Slide 16: Addressing Modes (cont’d)
Direct Addressing/Absolute addressing Mode
In this mode, effective address of operand is present in instruction itself.
For Example:
ADD R1, 4000
In this the 4000 is effective address of operand.
ADD AL,[0301]
Add the contents of offset address 0301 to AL.

## Slide 17: Addressing Modes (cont’d)
Indirect addressing Mode
In this mode address field of instruction contains the address of effective address. Here two references are required. 1st reference to get effective address. 2nd reference to access the data.
Based on the availability of Effective address, Indirect mode is of two kind:
Register Indirect: In this mode effective address is in the register, and corresponding register name will be maintained in the address field of an instruction. Here one register reference,one memory reference is required to access the data.
Memory Indirect: In this mode effective address is in the memory, and corresponding memory address will be maintained in the address field of an instruction. Here two memory reference is required to access the data.

## Slide 18: Addressing Modes (cont’d)
Indexed addressing mode
The operand’s offset is the sum of the content of an index register SI or DI and an 8 bit or 16 bit displacement.
Example
MOV AX, [SI +05]
Based Indexed Addressing
The operand’s offset is sum of the content of a base register BX or BP and an index register SI or DI.
Example:
ADD AX, [BX+SI]

## Slide 19: Instruction Types (cont’d)
Depending on operation they perform, all instructions are divided in several groups:
Arithmetic Instructions
Branch Instructions
Data Transfer Instructions
Logic Instructions
Bit-oriented Instructions

## Slide 20: Instruction Types (cont’d)
Arithmetic instructions
Arithmetic instructions perform several basic operations such as addition, subtraction, division, multiplication etc.
After execution, the result is stored in the first operand.
Example
ADD A, R1
The result of addition (A+R1) will be stored in the accumulator.

## Slide 21: Instruction Types (cont’d)
Branch Instructions
There are two kinds of branch instructions:
Unconditional jump instructions: upon their execution a jump to a new location from where the program continues execution is executed.
Conditional jump instructions: a jump to a new program location is executed only if a specified condition is met.
Otherwise, the program normally proceeds with the next instruction

## Slide 22: Instruction Types (cont’d)
Data Transfer Instructions
Data transfer instructions move the content of one register to another. The register the content of which is moved remains unchanged.
Example
MOV A, #data
Moves the immediate data to the accumulator

## Slide 23: Instruction Types (cont’d)
Logic Instructions
Logic instructions perform logic operations upon corresponding bits of two registers.
After execution, the result is stored in the first operand.
Example
CPL A
Complements the accumulator (1=0, 0=1)

## Slide 24: Instruction Types (cont’d)
Bit-oriented Instructions
Similar to logic instructions, bit-oriented instructions perform logic operations.
The difference is that these are performed upon single bits.
Example
CPL C
Complements the carry flag

## Slide 25: Assembly Language Programming (cont’d)
What is Assembly Language?
In computer programming, assembly language (or assembler language), often abbreviated ASM, is any low-level programming language in which there is a very strong correspondence between the instructions in the language and the architecture's machine code instructions.
Assembly code is converted into executable machine code by a utility program referred to as an assembler.
Assembly language uses a mnemonic to represent each low-level machine instruction or opcode.

## Slide 26: Assembly Language Programming (cont’d)
Why is ASM useful?
Machine language is a series of numbers, which is not easy for humans to read.
Using ASM, programmers can write human-readable programs that correspond almost exactly to machine language.
The disadvantage is that everything the computer does must be described explicitly, in precise detail.
The advantage is that the programmer has maximum control over what the computer is doing.

## Slide 27: Assembly Language Programming (cont’d)
Why should you learn Assembly Language?
Assembly language is not so widely used as most of the programming is done in high-level languages.
However, Assembly language is as close to the microprocessor you can get as a programmer.
Assembly language provides the programmer complete control over the resources of the system and helps amplify the performance and efficiency of the system.

## Slide 28: Assembly Language Programming (cont’d)
Why is ASM a "low-level" language?
Assembly is called a low-level programming language because there's (nearly) a one-to-one relationship between what it tells the computer to do, and what the computer does.
In general, one line of an assembly program contains a maximum of one instruction for the computer.

## Slide 29: Assembly Language Programming (cont’d)
How is ASM different from a "high-level" language?
High-level languages provide abstractions of low-level operations which allow the programmer to focus more on describing what they want to do, and less on how it should be done.
Programming this way is more convenient and makes programs easier to read at the sacrifice of low-level control.
Programs written in high-level languages will never match the raw speed and efficiency of programs written in assembly.
Examples of high-level languages include Python, Java, JavaScript, Clojure, and Lisp.

## Slide 30: Assembly Language Programming (cont’d)
Is ASM portable?
No.
Because assembly languages are tied to one specific computer architecture, they are not portable.
A program written in one assembly language would need to be completely rewritten for it to run on another type of machine.
Portability is one of the main advantages of higher-level languages.
The C programming language is often called "portable assembly" because C compilers exist for nearly every modern system architecture.
A program written in C may require some changes before it will compile on another computer, but the core language is portable.

## Slide 31: Assembly Language Programming (cont’d)
Assembly Language
A program written in assembly language consists of a series of mnemonic processor instructions and meta-statements (known variously as directives, pseudo-instructions and pseudo-ops), comments and data.
Assembly language instructions usually consist of an opcode mnemonic followed by a list of data, arguments or parameters.

## Slide 32: Assembly Language (cont’d)
Example
10110000 01100001
The above instruction tells an x86/IA-32 processor to move an immediate 8-bit value into a register.
The binary code for this instruction is 10110 followed by a 3-bit identifier for which register to use.
The identifier for the AL register is 000, so the following machine code loads the AL register with the data 01100001.
This binary computer code can be made more human-readable by expressing it in hexadecimal as follows.
B0 61
Here, B0 means 'Move a copy of the following value into AL, and 61 is a hexadecimal representation of the value 01100001, which is 97 in decimal.

## Slide 33: Assembly Language
Assembly language for the 8086 family provides the mnemonic MOV (an abbreviation of move) for instructions such as this, so the machine code above can be written as follows in assembly language, complete with an explanatory comment if required, after the semicolon.
This is much easier to read and to remember.
MOV AL, 61h
; Load AL with 97 decimal (61 hex)